SIXTH FRAMEWORK PROGRAMME NETWORK OF EXCELLENCE

Safety of Hydrogen as an Energy Carrier

Contract No SES6-CT-2004-502630

Definitions and Classifications

Deliverable D44 (WP 12)

Lead participant:	DNV

Partners			AirLiquide, GexCon, Hydro, HSE/HSL, INASMET, INERIS, 
				JRC, Risø, UNIPI

Dissemination level:	PP

Document version:	1.0

Date of preparation:	Feb 2006

CONTENTS

1.	Introduction	4

2.	Study basis	5

3.	recommended definitions and classifications	6

3.1.1	General definitions related to hydrogen safety (from ISO)	6

3.2 Definitions related to Risk Assessment	7

3.2.1	Definitions related to risk assessment (from ShapeRisk)	7

3.2.2	Definitions related to end points	7

3.3 Classifications of an incident that has occurred (recommended by HIAD)	8

4.	References	11

# Introduction

The safe introduction of hydrogen technologies and applications being the aim for the HySafe NoE, a common understanding of the term “safe” would definitely be a premise for success. In a philosophical context “safe” may be interpreted as “absence of danger”, but as this is not achievable in the real world, a technical interpretation of “safe” would rather be “danger is acceptably low”.

Harmonisation towards common risk acceptance criteria or a common understanding of what danger is acceptably low is one of the objectives for WP12. Subtask 12.1 was to initiate this work by mapping the status of risk acceptance criteria, identify gaps and suggest priorities for the further work towards common acceptance criteria for hydrogen safety.

As a part of this work we have identified a need for common definitions and classifications within HySafe NoE. This document is produced to facilitate a common understanding of essential terms. The intention is to extend the document with more specific terminology based on input from the entire HySafe network.

# Study basis

The basis for this work has been information from the EU 6th FP project SHAPE-RISK, Sharing Experience on Risk Management to Design Future Industrial Systems [1], as well as the work done in HySafe WP5 Hydrogen Incident and Accident Database [2].

Moreover, the ISO Guide 51 [3] and the ISO/TR15916 “Basic considerations for the safety of hydrogen systems” [4] has been used for more general terms.

# recommended definitions and classifications

### General definitions related to hydrogen safety (from ISO)

The following definitions are from the ISO documents [3] and [4].

| Acceptable risk, Tolerable risk | Risk which is accepted in a given context based on the current values of society |
| --- | --- |
| Blast wave | Intense pressure wave set in motion by the shock waves and hot product gases of a deflagration or detonation that impinges on the surroundings, typically air |
| BLEVE | Boiling Liquid Expanding Vapour Explosion |
| Confinement | Physical restriction, sufficient to influence the combustion process |
| Deflagration | Flame or chemical reaction moving through a flammable mixture at a rate less than the speed of sound in the unburned mixture |
| Detonation | Exothermic chemical reaction coupled to a shock wave that propagates through a detonable mixture or medium |
| Explosion | Rapid equilibrium of pressure between the region of energy release (system) and its surroundings |
| Flammability | Concentration of a fuel in an oxidizer below which a burning reaction cannot be sustained |
| Flammability limits | Lower (LFL) and upper (UFL) vapour concentration of fuel in a flammable mixture that will ignite and propagate a flame |
| Harm | Physical injury or damage to the health of people, or damage to property or the environment |
| Hazard | Potential source of harm |
| Ignite | Cause to burn or to catch fire |
| Ignition energy | Energy required to initiate flame propagation through a flammable mixture |
| Protective measure | Means used to reduce risk |
| Risk | Combination of the probability of occurrence of harm and the severity of that harm |
| Risk analysis | Systematic use of available information to identify hazards and to estimate the risk |
| Risk evaluation | Procedure based on the risk analysis to determine whether the tolerable risk has been achieved |
| Safety | Freedom from unacceptable risk |
| Shock wave | Large-amplitude compression wave in which there is a rapid and great change in density, pressure and particle velocity. |
| Stoichiometric mixture | Mixture of reactants in a chemical reaction that optimises production of the reaction products |
| Systematic risk management | An iterative process of risk assessment and risk reduction |
| Vapour cloud explosion | Gas explosion, flame moving through a flammable mixture of a fuel and an oxidizer |

## Definitions related to Risk Assessment

### Definitions related to risk assessment (from ShapeRisk)

| Hazard identification | To find the parts of the installation, which are of importance with respect to safety including mapping of the origin and causes of possible accidents and the quantities and properties of chemicals used. |
| --- | --- |
| Analysis of accident scenarios | To describe the possible modes how an accident can develop, e.g. a malfunction in a valve triggers other failure modes and gives a release of a dangerous compound to the environment threatening humans. |
| Analysis of frequencies and consequences | The accident scenarios are analysed more thoroughly. The probability of a scenario occurring and the consequences resulting from the scenario are calculated. The consequences are often measured as the impact on human health or mortality. Also, the environmental impacts might be used as a measure. |
| Evaluation of the total risk | The final evaluation of the risk includes a ranking of the scenarios found and might be expressed as a sum of the risk of all the scenarios. The probabilistic approach will define the risk as the product of the frequencies and the consequences. The deterministic approach is based on the possible consequences only. |

### Definitions related to end points

The ShapeRisk report concludes that directly or indirectly the majority of the surveyed countries use dose as end points of consequence calculations.

Effects of toxic substances:

| LC50 (Lethal Concentration 50) | The concentration in the air of a toxic substance, which may cause fatalities to the 50% of the population via inhalation of the substance for a duration of 30 minutes. [Equivalent dose D50=(LC50)n*30min where n depends on the substance]. |
| --- | --- |
| LC1 (Lethal Concentration 1) | The concentration in the air of a toxic substance, which may cause fatalities to the 1% of the population via inhalation of the substance for a duration of 30 minutes. [Equivalent dose D01=(LC1)n*30min where n depends on the substance]. |
| IDLH (Immediately Dangerous to Life and Health) | The maximum concentration in the air of a toxic substance in which can be exposed a person for 30 min without any irreversible for his/her health damages or injuries which can prevent him/her from leaving the area. |

Effects of Thermal Radiation

For the calculation of the dose in TDU (thermal dose unit: 1TDU = 1 (KW/m2)4/3*s) the following formula is used: D = Q4/3*t Q: the radiation intensity in W/m2 t: time in seconds

Effects of Overpressure

Given that the dose has a weak dependence on the duration of the shock wave, here peak overpressure is used instead of dose.

## Classifications of an incident that has occurred (recommended by HIAD)

The report “HIAD Specification and definition of its contents, operation and structure” [2] uses the below listed attributes to classify a hydrogen incident.

H2 Release (unwanted):

| Release type | Liquid or gas, compressed, mixtures |
| --- | --- |
| Release concentration | % H2 in carrying or surrounding medium |
| Release duration | In seconds From start of release to its containment. |
| Initial release rate | m3/s, alternatively in kg/s |
| Pressure of release source | bara/barg/psi |
| Release amount total | m3, alternatively in kg |

Release of other agents (unwanted):

| Release type | Liquid or gas |
| --- | --- |
| Name | Name of substance |
| Release concentration | (% in carrying or surrounding medium) |
| Release duration | (seconds) From start of release to its containment. |
| Initial release rate | (m3/s, alternatively in kg/s) |
| Release amount total | (m3, alternatively in kg) |

Consequences of event:

| Number of persons affected (directly) | On-site (to station personnel and to customers) Emergency/rescue personnel Off-site (to operators, to users, to other traficants and to residents) |
| --- | --- |
| Number of persons at risk | On-site (to station personnel and to customers) Emergency/rescue personnel Off-site (to operators, to users, to other traficants and to residents) |
| Fatalities | Distribute no of fatalities, part of body affected, etc as per "type of person" (position/function….). |
| Injuries | Distribute no of injuries, part of body injured/affected, type of/severity of injury, etc as per "type of person" (position/function) |
| Environmental/ecological damage | Long term and short term consequences including the extent/time of delay |
| Property loss (type) | Establishment/ plant/equipment |
| Property loss (type) | Surrounding property (direct costs) or 3rd party property |
| Economical loss (monetary) | Establishment/ plant - cost of damaged property, loss of production, reputation, trust, etc. |
| Economical loss (monetary) | Off-site property/3rd party - cost of damaged property, loss of production, reputation, trust, etc. |
| Cost of emergency response actions |  |
| Cost of clean-up and restoration |  |

# References

EU 6th FP: SHAPE-RISK,  Deliverable D 10 (D.2.C): Synthesis document on WP 2, February 28th 2005, http://shaperisk.jrc.it/index.html

HIAD Specification and definition of its contents, operation and structure, HySafe Deliverable No 22, ver 0.1, 1. June, 2005

ISO/IEC Guide 51:1999(E), Safety aspects – Guidelines for their inclusion in standards, edition 2, 1999

ISO/TR15916 “Basic considerations for the safety of hydrogen systems”